## Slide 2: New Requirements for Boat Fuel and Fuel Systems
IBEX
September 16, 2015
Speakers: Dave Marlow, Brunswick Boat Group,
Dan Ostrosky, Yamaha Motor Corp., Jeff Wasil, BRP/Evinrude, John McKnight, NMMA

## Slide 3: Disclaimer
Note: All references citing manufacturers of marine watercraft, engines and related equipment in this presentation are for informative and illustrative purposes only.
Their use in this presentation does not constitute an endorsement of these manufacturers or their products by the State of California or the California Air Resources Board.

## Slide 4
Purpose of ARB Regulation
California has the worst air quality in the nation
CARB develops regulations to comply with the federal Clean Air Act requirements
CARB’s new evaporative regulations for boats will fulfill a legal commitment included in California’s State Implementation Plan (SIP)
This regulation will help California obtain the emission reductions needed to attain federal ozone standards

## Slide 5: Who does this Regulation apply to?
CARB’s new evaporative emissions regulation applies to all MY 2018 spark-ignition marine watercraft with permanently installed fuel tanks sold in California
  Marine watercraft that use engines > 40HP must meet the more stringent CA standards
  Marine watercraft that use engines ≤ 40HP must meet harmonized existing U.S. EPA standards

## Slide 6: How it will work!
Fuel Hose Certified
by Component Mfg.
Tank Certified
by Component Mfg.
Canister Certified
by Component Mfg.
P.R.V. Certified
by Component Mfg.
Certified Components listed
on SIMW Component Web Page
Builder references Certified
Components from ARB Listing
ARB Certifies Watercraft
Using Components EO’s
in lieu of Components Data

## Slide 7: Component Certification
What is component certification?
  Component certification is the certification of fuel hoses, fuel tanks, carbon canisters and prv by ARB
  Certification means that manufacturers have demonstrated that their product meets applicable design and performance requirements

## Slide 8: Design Based Standards < 30kW (40HP)
 | Fuel Hose Permeation (grams/m2/day ROG) | Fuel Tank Permeation (grams/m2/ day ROG ) | Diurnal Requirement (grams/gallon/ day HC) | Fuel Injection or Equivalent (grams/hour)
Standards for MY2018 and later | 15.0 | 1.5 | 0.4 | None
Test Procedure | 40 CFR §1060.515 | 40 CFR §1060.5201 | 40 CFR §1060.525 | None
1 As an alternative, fuel tanks can be certified to 2.5 grams/m2/day at 40°C
All evaporative emission standards and test procedures have been harmonized with U.S. EPA

## Slide 9: Design Based Standards > 30kW (40HP) (Trailerable)*
*Applicable to marine watercraft ≤ 26 ft. in length and ≤ 8.5 ft.in width
 | Fuel Hose Permeation (grams ROG/m2/day) | Fuel Tank Permeation (grams ROG/m2/day) | Diurnal Tank Venting Loss Requirement (grams HC/gallon/day) |  | Meet Fuel Injection Definition or Equivalent Performance Standard (grams HC/hour)
 |  |  | Canister1 | Non-Canister | 
Standards for MY2018 and MY2019 | 10.0 | 0.70 | 0.25 | 65% reduction from uncontrolled HC emissions | 0.4
Standards for MY2020 and later | 5.02 | 0.70 | 0.25 | 65% reduction from uncontrolled HC emissions | 0.4
Test Procedure | TP-1504 or SAE J1737 | TP-15043 | TP-1503 |  | TP-1502
1 Canisters may be certified by design as an option. Canisters must have a minimum butane working capacity of 3.8 grams/gallon
2 Must be performed at 40°C
3 As an alternative, fuel tanks can be certified to 1.4 grams/m2/day at 40°C

## Slide 10: Pathways to Compliance
  CARB’s new regulation has two methods for demonstrating compliance (13 CCR 2855 (a)):
  Design-Based – Requires marine watercraft manufacturer to use specific CARB-certified components for:
      Fuel injection
      Low permeation fuel hoses
      Low permeation fuel tank
      Passively-purged carbon canister or pressure relief valve
      Performance Alternative – Requires manufacturers
      to meet one standard for the complete boat or fuel system, based on a 24-hour diurnal test (TP-1501, TP1502)

## Slide 11: New Testing Procedures (TP’s)
ARB will implement the following New Test Procedures or “TP’s” for component Compliance testing:
TP1501 - Hot Soak for Diurnal Emissions for SIMW
TP1502 - Hot Soak for Evaporative Emissions SIMW
TP1503 - Diurnal Venting Emissions Carbon Canister, PRV
TP1504 - Permeation Emissions form Fuel Tanks, Hoses and Caps
TP1505 – Durability and compliance testing for PRV
Most TP’s follow existing Federal Test requirements
What else is different??
All sample groups must test 5 samples (2 more than current EPA)
Requirements to include CAD drawings where applicable

## Slide 12: Component Test Limitations
ARB will require the following as Worst Case: EPA 1060.235 (b) (1)
Fuel Hose - smallest inside diameter
Fuel Tank – smallest volume to surface area ratio
Carbon Canister – canister sized for the largest fuel tank in category
PRV ( pressure relief valve) – meets minimum design requirements and additional durability testing

## Slide 13: Basic Component Certification Rules
Must include testing of 5 components samples (Current EPA is 3 samples)
Application Must be deemed complete by ARB before it can be processed
ARB will issue a component Executive order (EO) for each component
ARB will update Web site with New EO’s periodically
Note: Engine Manufacturer has the responsibility for certification of fuel injection system. (Will be part of Engine Family EO)

## Slide 15: Fuel Hose Certification (case study)
Example:
A fuel hose manufacturer seeks a component EO for low permeation fuel hoses with internal diameters ranging in size from 1/4 to 3/8 inches

## Slide 16: Fuel Hose Certification Case study
Letter of Intent (on company letterhead) must include:
Specific request for an EO for the component
Description of the barrier material and thickness
Emissions data results from five (5) component samples (in-house or third-party testing)
Reference to the test procedure used to generate the data
Reference to the test temperature and test fuel used generate the data
Letter signed by authorized company representative

## Slide 17: Case Study “Hose” cont’d
Letter should also include:
Description of material composition
General description of the manufacturing process
Drawing of component (labeled parts and cross-section, general dimension measurements, intended placement of EO labeling, etc.)
Installation and maintenance instructions (if applicable)
Limits for proper functioning (e.g., temp range, ethanol %, bend radius, etc.)
Warranty statement (ARB Verbatim or Pre Approved language)
Other pertinent information (e.g., quality control frequency, fluorination level verification, etc.) Note: Detail QA process

## Slide 18: Case Study “Hose” cont’d
Hose emissions data from five (5) samples
Declaration of how the test data was generated (Hose was tested at a constant 23°C with CE10 following TP-1504)
General material description of the hose along with labeled CAD drawings
Location and mounting instructions ***
Any conditions which might affect the hose’s integrity (maximum skin temperature, kinking radius, etc.) ***

## Slide 19: Submission
Manufacturer submits package requesting a component EO, test data, and other required info to:
California Air Resources Board
Monitoring and Laboratory Division
Attn: Division Chief
P.O. Box 2815
Sacramento, CA 95812

## Slide 20
NOW WHAT???

## Slide 22: ARB Processing
Logging the date of receipt
Reviewing the application for completeness
Notifying applicant if not complete (within 30 days)
Verifying that 5 hose sample data points are below the design criteria of 10 grams/meter2/day
Drafting a component EO for the hoses
Mailing the component EO to the manufacturer
Adding the component EO to SIMW Component Web Page
http://www.arb.ca.gov/msprog/offroad/sore/sorecomponent/sorecomponent.htm

## Slide 23: Certification Timing
ARB can take up to 90 days for complete process
90 day clock does not start until a complete application is received and verified.
Be sure all elements of your application are included and readable to reduce certification delays.

## Slide 24: Post Certification
ARB may conduct compliance testing on Components
Component manufacturer and boat builder will be notified if a component fails compliance testing
    EO may be revoked
    Penalties may be imposed (Component Mfg.)
Component EO is valid until revoked
Any emissions-related change to the component must be submitted and reviewed by CARB

## Slide 25: Post Certification
Running Changes:
Non emission affected: Part number, Color, labeling etc…
Submit simple explanation to ARB identifying changes so to be added to ARB EO file
Note: Should be done annually prior to production
Major Design changes, material thickness, type, brand, mfg. process..
Will require new application and EO

## Slide 26: ARB Contact List
Scott Monday – Regulations and Test Procedures
(916) 445-9319, scott.monday@arb.ca.gov
Michele Dunlop – Component Certification
(916) 323-8971, michele.dunlop@arb.ca.gov
Kevin Curley – Boat Certification
(626) 350-6418, kevin.curley@arb.ca.gov
Details about the new evaporative requirements, test procedures, and application process can be found on CARB’s Recreational Marine Activities website:
http://www.arb.ca.gov/msprog/offroad/recmarine/recmarine.htm

## Slide 27: Component Certification
?
Thanks for listening , any questions ?
dan_ostrosky@yamaha-motor.com
714-761-7715

## Slide 28: CARB Boat Certification
What is boat certification?
  Boat builders demonstrate their product meets evaporative requirements
    Upon completion, a CARB EO is issued to allow sale of boat into California
  Boat builders certify an evaporative family
    One application per evaporative family
    An evaporative family can cover many models that utilize same type of components

## Slide 29
Evaporative System Certification Overview
What needs to be certified?
  All marine watercraft with installed fuel tanks that use spark- ignition marine engines sold in California must be certified annually
Who can certify?
  Engine manufacturers (Honda Marine, Mercury Marine, Yamaha, etc.), or
  Boat builders (Crestliner, Bayliner, Mastercraft, etc.)
  Fuel System Builders/Integrators
  Dealers

## Slide 30: CARB Boat Certification Process
How do I certify my boat?
  Plan model(s) design
  Group models into an evaporative family
  Submit application
  Receive Executive Order
  Sell boat in California
Why is CARB boat evaporative certification required?
  Provides a formal legal document (EO) showing that the boat is compliant with CARB evaporative requirements
A boat builder may build the boat at any point in the process, however the boat must be certified before it is sold in California

## Slide 31
CARB Boat Evaporative Certification Process
Design-Based

## Slide 32: Boat Builder Planning
Boat builders should plan the design of the evaporative system in advance
  May have third party design evaporative system
  If models remain the same as previous year, boat builders may submit previous information
Once a design has been established, the boat builder can apply for certification

## Slide 33: Boat Builder Responsibilities
Boat builders demonstrate their evaporative system meets requirements
  Design fuel system using CARB certified components
  Placement and integration of evaporative components
  Proper installation of complete evaporative system
  Labeling and warranty
  Other requirements
  Obtain CARB EO

## Slide 34: Boat Builder Application Process
Design-Based Application - Start of Model Year
  Boat builders submit one application for each evaporative family
  Boat builder may submit an application at any time after they know the model design
  On the application, reference the component EO numbers applicable to each evaporative component used in the evaporative family
  Submit the application electronically to CARB
  CARB reviews application and, if compliant, issues an EO

## Slide 35: Evaporative Family
What is an evaporative family?
  Evaporative family means a class of evaporative components used on boats with similar fuel system characteristics
  Evaporative families have similar fuel hose types, fuel tank types, carbon canister sizes, etc.
Characteristics of evaporative families
  Vented control: carbon canister vs. pressure relief valve
  Fuel tank types: metal vs. plastic
  Fuel hose types: U.S. EPA vs. CARB
  Boat size: trailerable vs. nontrailerable

## Slide 36: Evaporative Family
All models that have these characteristics are considered one evaporative family and need only one certification application
Example – Single Evaporative Family
Fuel System Design | Evaporative Family Type
Fuel Hose Type | A1-15
Fuel Tank Type | Plastic
Vent Type | Carbon Canisters 0.5L – 0-60 gallons 0.75L – 62-93 gallons 1.0L – 93-124 gallons
Trailerable or Nontrailerable | Trailerable

## Slide 37: Evaporative Family
Models using plastic tanks will be in one evaporative family; models using metal tanks will be in a second family
Example – Two Evaporative Families
Fuel System Design | Evaporative Family Type
Fuel Hose Type | A1-15
Fuel Tank Type | Plastic or Metal
Vent Type | Carbon Canisters 0.5L – 0-60 gallons 0.75L – 62-93 gallons
Trailerable/Nontrailerable | Trailerable

## Slide 38: Design-Based System Certification
How is design-based certification useful?
  Allows boat builders to show compliance without testing the complete evaporative system in a sealed housing for evaporative determination enclosure (SHED)
  Reduces costs of testing
  Reduces lead testing time

## Slide 39: Boat Builder Responsibilities after Certification
Must re-apply for certification each model year
Notify CARB of changes using running change process
  Changes to evaporative design
  Model additions
Boat builder is not responsible for noncompliant component

## Slide 40: Optional Design-Based Conditional EO Certification Process
Boat builder submits a compliance letter and requests a conditional EO
CARB quickly issues EO within 30 days so boat builder can sell in CA without delay
Boat builder must submit full design-based application within 90 days
If boat builder does not submit full design-based application within 90 days, CARB revokes EO

## Slide 41: Boat Label & Warranty
Labels and warranty statements may be approved ahead of time
Approval remains valid for future model years provided no changes are made
CARB has provided templates for evaporative emissions labels and warranty statements

## Slide 42
Boat Certification Application Templates
Draft application, label, and warranty templates for design-based boat certification are attached
Boat Certification workshop anticipated to be held mid 2016
  Present certification forms and processes
  Solicit industry input and get feedback
Finalized application templates will be issued after workshop

## Slide 43: Presentation Outline
Section 1: Background
Section 2: Component Certification Section 3: Boat Certification Section 4: Industry Cooperation

## Slide 44
Cooperation with NMMA/ABYC to Date
NMMA has been actively engaged with CARB
  Working with CARB since 2006
  Actively participated in all CARB marine workshops
  Helped to understand the unique manufacturing process of the boat building industry
  Organized face-to-face meeting with ABYC, industry representatives, and boat builders
  Organized boat builder manufacturing tour
  Helped streamline CARB marine certification
  Provided information about current NMMA certification process

## Slide 45: Alternate CARB Evaporative Certification Process streamlined with NMMA
- - - - Alternate path for NMMA members

## Slide 46: Anticipated Implementation Schedule
Late 2016: Begin Submitting Component Applications
2017:
Begin Submitting Watercraft Applications
MY 2018:
SIMW Regulation Implemented
Early 2016:
Begin Testing Boat Certification
Components
Mid 2016:
Workshop

## Slide 47
Spark-Ignition Marine Watercraft (SIMW) Design-Based Certification Templates
(Applicable to 2018 MY and Later Watercraft)
ARB has developed a streamlined design-based certification process for boat builders to certify SIMW and receive a California Executive Order (EO). Specifically, boat builders who want to sell in California should follow one of the following options:
Option 1 - One-step Design-Based Certification Process:
Boat builder (or NMMA acting on their behalf) must submit a full application and receive an EO before offering boats for sale in California. Please find listed below the documents that boat builders must submit as part of the certification application:
Full Design-Based Certification Application
(See Attachment: “DESIGN-BASED CERTIFICATION APPLICATION”)
Sample combined U. S. Coast Guard/NMMA/ARB/EPA emissions label format template (See Attachment: “SAMPLE CALIFORNIA EVAPORATIVE EMISSIONS LABEL”)
Sample California emissions warranty statement template
(See Attachment: “CALIFORNIA EVAPORATIVE EMISSION CONTROL WARRANTY STATEMENT”)
Option 2 - Two-step Design-Based Conditional EO Certification Process:
Please see attached flow-chart titled “Draft Proposed SIMW Optional Conditional EO Certification Process” describing the two-step design-based conditional EO certification process. The two main steps are:
Boat builder (or NMMA acting on their behalf) must submit a signed statement of compliance letter and receive interim approval (a conditional EO, which will be issued within 30 days of receipt of the compliance letter) before offering boats for sale in California
(See Attachment: “DESIGN-BASED CONDITIONAL CERTIFICATION COMPLIANCE LETTER”)
Boat builder (or NMMA acting on their behalf) must submit a full application (including all three documents listed above in Option 1) within 90 days of the signed statement of compliance letter and receive an EO as in the one-step process.

## Slide 48
NOT FINAL
DESIGN-BASED CONDITIONAL CERTIFICATION COMPLIANCE LETTER
(APPLICABLE TO 2018 MY & LATER WATERCRAFT)
Manufacturer’s Letterhead
Date
Chief, Emissions Compliance, Automotive Regulations and Science Division Air Resources Board
9480 Telstar Avenue, Suite 4 El Monte, California 91731
XYZ Company (the manufacturer’s legal name) hereby requests that its 20XX model year new spark- ignition marine watercraft be conditionally certified by ARB based on the compliance statements in this letter and on its commitment to provide any information needed to demonstrate full compliance with the California emission standards for new spark-ignition marine watercraft.
XYZ Company hereby makes the following statements of compliance regarding the 20XX model year evaporative certification of all of its spark-ignition marine watercraft models:
Conformance with the general standards and test procedure requirements specified in Title 13, Chapter 5, Article 14, sections 2850-2871 of the California Code of Regulations (CCR).
Conformance with the labeling (2860), warranty (2861 & 2862), tamper resistance (2856(e)), and fuel
injection or equivalent performance standard (2855(a)) requirements as required in 13 CCR.
Conformance with the Deck Fill Plate Compatibility Standard as required in 13 CCR, Section 2855(b)(1) and with the California Fuel Compatibility Standard as required in 13 CCR, Section 2855(b)(2).
The XYZ Company’s production will consist of the following watercraft types: (Personal Watercraft,
Outboard, Inboard, Sterndrive, Jetboat, Other). The watercraft will be (Trailerable ≤26ft, Nontrailerable >26ft).
Production evaporative systems shall be in all material respects the same as those for which certification is submitted.
The completed evaporative certification application demonstrating compliance will be submitted to ARB within 90 days of the date of this letter.
No watercraft will be introduced into commerce in California before the conditional Executive Order is issued.
XYZ Company will demonstrate compliance with all applicable California evaporative emission standards and requirements, including submission of a complete certification application, within 90 days of the date of this letter. XYZ Company understands that failure to adequately demonstrate compliance by the above specified date shall be cause for the Air Resources Board to revoke the conditional Executive Order, in which event any watercraft introduced into commerce under the revoked conditional Executive Order shall be deemed uncertified, and which may subject XYZ Company to enforcement actions. The projected start date for introduction into commerce in California is MM/DD/YYYY.
If you have any questions, please contact me at xxx-xxx-xxxx. Sincerely,
Manufacturer Representative’s Name
Title
Mailing Address Phone Number Email
Revised 7/21/15

## Slide 49
NOT FINAL
DESIGN-BASED CERTIFICATION APPLICATION
(APPLICABLE TO 2018 MY & LATER WATERCRAFT)
Date
Chief, Emissions Compliance, Automotive Regulations and Science Division Air Resources Board
9480 Telstar Avenue, Suite 4 El Monte, California 91731
Evaporative Family Name: XXXXXXXXXXXX Application Type: _ New Running Change
XYZ Company hereby submits the certification application and makes the following statements of compliance regarding the 20XX model year certification of its spark-ignition marine watercraft.
Conformance with the general standards and requirements as required in Title 13, Chapter 5, Article 14, sections 2850-2871 of the California Code of Regulations.
Conformance with the Deck Fill Plate Compatibility Standard as required in 13 CCR, Section 2855(b)(1) and with the California Fuel Compatibility Standard as required in 13 CCR, Section 2855(b)(2).
Conformance with the labeling and warranty requirements as required in 13 CCR, Sections 2859, 2860, 2861,
and 2862.
Conformance with the fuel injection definition or equivalent performance standard and tamper resistance requirements as required in 13 CCR, Sections 2855(a) and 2856(e), respectively.
Production evaporative systems shall be in all material respects the same as those for which certification is granted.
Installation will be completed as directed by the component manufacturer and will adhere to the specifications within the referenced component Executive Order(s).
If you have any questions, please contact me at xxx-xxx-xxxx. Sincerely,
Manufacturer Representative’s Name
Title
Page 1 of 2
Revised 7/21/15
Fuel Tank Executive Order(s) | Fuel Line Executive Order(s) |  | Carbon Canister/Venting System (Diurnal) Executive Order(s) | 
List ARB EO number(s) | List ARB EO number(s) |  | List ARB EO number(s) | List Fuel Tank Range
 |  |  | List ARB EO number(s) | List Fuel Tank Range
Manufacturer Contact Contact: Title: Company: Address: City, State, Zip Phone No.: Fax No.: Email: |  | Production Plant Location/Contact Contact: Title: Company: Address: City, State, Zip Phone No.: Fax No.: Email: |  | 
Watercraft Type Personal Watercraft Outboard Inboard Sterndrive Jetboat Other: _ |  | Watercraft Specifications Trailerable (≤26ft) _ Nontrailerable (>26ft) Less than 30kW Greater than 30kW |  | 
 |  | Evaporative Warranty/Label Approvals Label Approval #: NMC-2018-XXXX Warranty Approval #: NMC-2018-XXXX |  | 
Confidential Information a) Projected California sales(units): b) Projected 50-State Sales (units): _ c) Introduction into commerce date: |  |  |  | 

## Slide 50
NOT FINAL
SAMPLE CALIFORNIA EVAPORATIVE EMISSIONS LABEL (COMBINED WITH US EPA, NMMA, AND USCG)
Revised 2/25/15